## Slide 1
Deflection as result of Cryo cooling process (25C->-182C)
Maximum x Deflection: ~-0.01374 inches
Maximum y Deflection: ~-0.0056 inches
Simple 2D approximation of Ring:
2” Diameter
0.125” thickness
Boundary Conditions:
Symmetry x restrictions
All rotation restricted

## Slide 2
X Direction Maximum Deflection: ~-0.014 inches
Z Direction Maximum Deflection: ~ -0.015 inches
Deflection as result of Cryo Cooling process (25C->-182C)
Boundary Conditions: Restricted Vertical (y) movement, Restricted all rotation
6061-T6 Aluminum

## Slide 3
Stress Concentrations (Von Mises Stress)
-based on assumed boundary conditions displayed to the right
-fixed in y, all rotation fixed
-using 2403 element Tet-Quad mesh
Mises stress concentrations appear in red to the left

## Slide 4
Updated to 3905 element mesh
Steady-state Temperature distribution to be used with Stress Analysis (Degrees C): 25C outer to -182C inner Temps
Maximum deflection values show similar results to previous mesh analysis:
Max X: ~0.0174”
Max Z: ~0.017”

## Slide 5
3905 Element Mesh Stress Concentrations (Von Mises):
Assuming same previous boundary conditions
Build-up on inner edge of mating ring
Tensile/compressive stress concentrations:

## Slide 6
Steady State Endcap Temperature Gradient for use with Steady State Temp analysis (Degrees C):
Blue regions= -182C
Red Regions= 25C
Temperature gradient viewed on edge regions in between
5317 Element tet-quad mesh

## Slide 7
Boundary Conditions for Preliminary Stress analysis:
-All rotation restricted
-Y direction restricted along bottom edges of endcap
Material Properties:
6061-T6 Aluminum
Young’s Modulus = 69 Gpa
Poisson’s Ratio = 0.29
Conductivity @ 25C = 152 W/m*K
Thermal Expansion Coeff = 23.4e-6 m/m*C
Convection Coeff to air =10-100 W/m^2*K

## Slide 8
Displacement Analysis using these BC’s:
Y Direction w/ Deformed shape superimposed
Max Y: 0.00702”
Max X: 0.009886”
Max Z: 0.008142”
Red & Blue regions represent locations of maximum displacements, with appropriate gradients in between

## Slide 9
Stress Concentrations with 5317 tet-quad Mesh:
Von Mises Stress
Tensile/Compressive (S11)

## Slide 10
Analysis repeated with 6489 Element Mesh:
Temperature Gradient:
Same material properties & boundary conditions
Red regions = 25C
Blue regions = -182C

## Slide 11
6489 Element Stress Concentrations:
Shows same concentration pattern across both meshes..
Von Mises
Tensile/Compressive (S11)

## Slide 12
Displacement results somewhat inconclusive using higher element mesh...need to re-examine boundary conditions..
U1 (X) & U3 (Z) values much larger than previous mesh, U2 (Y) correlates
Max x: ~0.026”
Max y: ~0.0071”
Max z: ~0.019”